## Slide 1: Array Processors

## Slide 2: Introduction
Major characteristics of SIMD architectures
  A single processor(CP)
  Synchronous array processors(PEs)
  Data-parallel architectures
  Hardware intensive architectures
  Interconnection network

## Slide 3: Associative Processor
An SIMD whose main component is an associative memory.
AM(Associative Memory)
  Used in fast search operations
  Data register
  Mask register
  Word selector
  Result register

## Slide 4: Introduction(continued)
Associative processor architectures also belong to the SIMD classification.
  STRAN
  Goodyear Aerospace’s MPP(massively parallel processor)
The systolic architectures are a special type of synchronous array processor architecture.

## Slide 5: SIMD Organization
  SIMDs offer an N-fold throughput enhancement over SISD provided the application exhibits a data-parallelism of degree N.
Memory
  Data are distributed among the memory blocks
  A data alignment network allows any data memory to be accessed by any PE.

## Slide 6: SIMD Organization (continued)
Control processor
  To fetch instructions and decode them
  To transfer instructions to PEs for executions
  To perform all address computations
  To retrieve some data elements from the memory
  To broadcast them to all PEs as required.

## Slide 7: SIMD Organization (continued)
Arithmetic/Logic processors
  To perform the arithmetic and logical operations on the data
  Each PE corresponding to data paths and arithmetic/logic units of an SISD processor capable of responding to control control signals from the

## Slide 8: SIMD Organization (continued)
Registers, instruction set, performance considerations
  The instruction set contains two types of index manipulation instructions, one set for global registers and the other for local registers

## Slide 9: Data Storage Techniques and Memory Organization
Straight storage / skewed storage
GCD

## Slide 10: Interconnection Networks
Terminology and performance measures
  Nodes
  Links
  Messages
  Paths: dedicated / shared
  Switches
  Directed(or indirect) message transfer
  Centralized (or decentralized) indirect message transfer

## Slide 11: Interconnection Networks (continued)
Terminology and performance measures
  Performance measures
    Connectivity
    Bandwidth
    Latency
    Average distance
    Hardware complexity
    Cost
    Place modularity
    Regularity
    Reliability and fault tolerance
    Additional functionality

## Slide 12: Interconnection Networks (continued)
Routing protocols
  Circuit switching
  Packet switching
  Worm hole switching
Routing mechanism
  Static / dynamic
Switching setting functions
  Centralized / distributed

## Slide 13: Interconnection Networks (continued)
Static topologies
  Linear array and ring
  Two dimensional mesh
  Star
  Binary tree
  Complete interconnection
  hypercube

## Slide 14: Interconnection Networks (continued)
Dynamic topologies
  Bus networks
  Crossbar network
  Switching networks
    Perfect shuffle
      Single stage
      Multistage

## Slide 15: Performance Evaluation and Scalability
The speedup S of a parallel computer system:
Theoretically, the maximum speed possible with a p processor system is p. ( A superlinear speedup is an exception)
  Maximum speedup is not possible in practice, because all the processors in the system cannot be kept busy performing useful computations all the time.

## Slide 16: Performance Evaluation and Scalability (continued)
The cost is the product of the parallel run time and the number of processors.
  Cost optimal: if the cost of a parallel system is proportional to the execution time of the fastest algorithm.
Scalability is a measure of its ability to increase speedup as the number of processors increases.

## Slide 17: Programming SIMDs
The SIMD instruction set contains additional instruction for IN operations, manipulating local and global registers, setting activity bits based on data conditions.
Popular high-level languages such as FORTRAN, C, and LISP have been extended to allow data-parallel programming on SIMDs.

## Slide 18: Example Systems
ILLIAC-IV
  The ILLIAC-IV project was started in 1966 at the University of Illinois.
  A system with 256 processors controlled by a CP was envisioned.
  The set of processors was divided into four quadrants of 64 processors.
  The PE array is arranged as an 8x8 torus

## Slide 19: Example Systems (continued)
CM-2
  Processors
    The 16 processors are connected by a 4x4 mesh.
  Hypercube
    The processors are linked by a 12-dimensional hypercube router network.
    The following parallel communication operations permit elements of parallel variables: reduce & broadcast, grid(NEWS), general(send, get), scan, spread, sort

## Slide 20: Example Systems (continued)
CM-2
  Nexus
    A 4x4 crosspoint switch,
  Router
    It is used to transmit data from a processor to the other.
  NEWS Grid
    A two-dimensional mesh that allows nearest-neighbor communication.

## Slide 21: Example Systems (continued)
CM-2
  Input/Output system
    Each 8-K processor section is connected to one of the eight I/O channels .
    Data is passed along the channels to I/O controller (Figure 5.27).
  Software
    Assembly language, Paris
    *LISP, CM-LISP, and *C

## Slide 22: Systolic Arrays
A systolic array is a special purpose planar array of simple processors that feature a regular, near-neighbor interconnection network.

## Slide 23: Example Systems (continued)
CM-2
  The CM-2, introduced in 1987, is a massively parallel SIMD machine.
  Table 5.1 summarizes its characteristics.
  Figure 5.23 shows the architecture of CM-2.