## Slide 1: NETWORK LAYER

## Slide 2: OVERVIEW
Routing Algorithms
  Shortest Path
  Flooding
  Flow-based
  Distance Vector
  Link State
  Hierarchical
  Broadcast
  Multicast
  Routing for Mobile Hosts
Congestion control
IP Addressing
Routers

## Slide 3: ROUTING ALGORITHMS 1. Shortest Path
A
C
D
B
E
F
B(A,2)
A(-,-)
E(A,2)
C(B,3)
D(E,3)
F(E,4)
2
2
1
2
1
1
3
3
A – E – D – F
A – E – F is the answer.

## Slide 4: ROUTING ALGORITHMS
To prevent packets from circulating indefinitely, a packet has a hop counter. Every time a packet arrives at an IMP, the hop counter is decrease by 1. Once the hop counter of a packet reaches 0, the packet is discarded.
Packet
2. Flooding
IMP
B
Packet to IMP C
Packet to IMP D
Packet to IMP E

## Slide 5: IP ADDRESSING
Format
x x x x x x x x . x x x x x x x x . x x x x x x x x . x x x x x x x x
where x is either 0 or 1
Example 1:
1 1 1 1 1 1 1 1 . 1 1 1 1 1 1 1 1 . 0 0 0 0 0 0 0 0 . 0 0 0 0 0 0 0 0
255.255.0.0
Example 2:
1 1 1 1 1 1 1 1 . 1 1 1 1 1 1 1 1 . 1 0 0 0 0 0 0 0 . 0 0 0 0 0 0 0 0
255.255.192.0

## Slide 6: IP ADDRESSING
Network Address
Example 1:
IP address of computer 180.100.7.1
Mask 255.255.0.0
Network address 180.100.0.0
Example 2:
IP address of computer 180.100.7.1
Mask 255.255.255.0
Network address 180.100.7.0
Example 3:
IP address of computer 180.100.7.2
Mask 255.255.192.0
Network address 180.100.0.0

## Slide 7: IP ADDRESSING
Mask
Valid mask are contiguous 1’s from left to right.
Examples:
  Valid
  255.0.0.0
  255.255.0.0
  255.255.255.0
  Invalid
  255.1.0.0
  255.0.255.0
  255.255.64.0
  200.255.0.0

## Slide 8: IP ADDRESSING
Subnets
The Internet is running out of IP address. One solution is to subnet a network address.
This is done by borrowing host bits to be used as network bits.
Example:
Class B mask 255.255.0.0
Borrowing 1 bit gives a subnet mask of 255.255.128.0
Borrowing 2 bits gives a subnet mask of 255.255.192.0
Borrowing 3 bits gives a subnet mask of 255.255.224.0
Borrowing 4 bits gives a subnet mask of 255.255.240.0

## Slide 9: IP ADDRESSING
Example:
Given an IP address of 180.200.0.0, subnet by borrowing 4 bits.
Subnet mask = 255.255.240.0
The 4 bits borrowed are value 128, 64, 32, 16. This will create 16 sub networks, where the first and last will be unusable.
Sub network address:
  180.200.0.0
  180.200.16.0
  180.200.32.0
  180.200.48.0
  180.200.64.0
  etc…

## Slide 10: IP ADDRESSING
The first 3 usable sub networks are:
180.200.16.0
180.200.32.0
180.200.48.0
For sub network 180.200.16.0, the valid IP address are:
180.200.16.1 to 180.200.31.254
Directed broadcast address is:
180.200.31.255

## Slide 11: Thankyou