## Slide 1: Parallel Processing Architectures
Vivek Shrivastava

## Slide 2: Parallel Computers
Definition: “A parallel computer is a collection of processing elements that cooperate and communicate to solve large problems fast.”
Questions about parallel computers:
  How large a collection?
  How powerful are processing elements?
  How do they cooperate and communicate?
  How are data transmitted?
  What type of interconnection?
  What are HW and SW primitives for programmer?
  Does it translate into performance?

## Slide 3: Parallel Processors “Myth”
The dream of computer architects since 1950s: replicate processors to add performance vs. design a faster processor
Led to innovative organization tied to particular programming models since “uniprocessors can’t keep going”
  e.g., uniprocessors must stop getting faster due to limit of speed of light – Has it happened?
  Killer Micros! Parallelism moved to instruction level. Microprocessor performance doubles every 1.5 years!
  In 1990s companies went out of business: Thinking Machines, Kendall Square, ...

## Slide 4: What level Parallelism?
Bit level parallelism: 1970 to ~1985
  4 bits, 8 bit, 16 bit, 32 bit microprocessors
Instruction level parallelism (ILP): ~1985 through today
  Pipelining
  Superscalar
  VLIW
  Out-of-Order execution
  Limits to benefits of ILP?
Process Level or Thread level parallelism; mainstream for general purpose computing?
  Servers are parallel
  High-end Desktop dual processor PC

## Slide 5: Why Multiprocessors?
Microprocessors as the fastest CPUs
  Collecting several much easier than redesigning 1
Complexity of current microprocessors
  Do we have enough ideas to sustain 2X/1.5yr?
  Can we deliver such complexity on schedule?
  Limit to ILP due to data dependency
Slow (but steady) improvement in parallel software (scientific apps, databases, OS)
Emergence of embedded and server markets driving microprocessors in addition to desktops
  Embedded functional parallelism
  Network processors exploiting packet-level parallelism
  SMP Servers and cluster of workstations for multiple users – Less demand for parallel computing

## Slide 7: Amdahl’s Law and Parallel Computers
A portion is sequential => limits parallel speedup
  Speedup <= 1/ (1-FracX)
Ex. What fraction sequetial to get 80X speedup from 100 processors? Assume either 1 processor or 100 fully used
80 = 1 / [(FracX/100 + (1-FracX)]
0.8*FracX + 80*(1-FracX) = 80 - 79.2*FracX = 1
FracX = (80-1)/79.2 = 0.9975
Only 0.25% sequential!

## Slide 9: Classification of Computer Systems Flynn’s Classification
SISD (Single Instruction Single Data)
  Uniprocessors
MISD (Multiple Instruction Single Data)
  ???; multiple processors on a single data stream
SIMD (Single Instruction Multiple Data)
  Examples: Illiac-IV, CM-2
    Simple programming model
    Low overhead
    Flexibility
    All custom integrated circuits
  (Phrase reused by Intel marketing for media instructions ~ vector)
MIMD (Multiple Instruction Multiple Data)
  Examples: Sun Enterprise 5000, Cray T3D, SGI Origin
    Flexible
    Use off-the-shelf micros
MIMD current winner: Concentrate on major design emphasis <= 128 processor MIMD machines

## Slide 10: Classification of Parallel Processors
SIMD – EX: Illiac IV and Maspar
MIMD - True Multiprocessors
1. Message Passing Multiprocessor: Interprocessor communication through explicit “send” and “receive” operation of messages over the network
EX: IBM SP2, NCUBE, and Clusters
2. Shared Memory Multiprocessor: Interprocessor communication by load and store operations to shared memory locations.
EX: SMP Servers, SGI Origin, HP
V-Class, Cray T3E

## Slide 11: Shared Address/Memory Model
Communicate via Load and Store
  Oldest and most popular model
Based on timesharing: processes on multiple processors vs. sharing single processor
Single virtual and physical address space
  Multiple processes can overlap (share), but ALL threads share a process address space
Writes to shared address space by one thread are visible to reads of other threads
  Usual model: share code, private stack, some shared heap, some private heap

## Slide 12: Shared Address Model Summary
Each process can name all data it shares with other processes
Data transfer via load and store
Data size: byte, word, ... or cache blocks
Uses virtual memory to map virtual to local or remote physical
Memory hierarchy model applies: now communication moves data to local proc. cache (as load moves data from memory to cache)
  Latency, BW (cache block?), scalability when communicate?

## Slide 13: Message Passing Model
Whole computers (CPU, memory, I/O devices) communicate as explicit I/O operations
Send specifies local buffer + receiving process on remote computer
Receive specifies sending process on remote computer + local buffer to place data
  Usually send includes process tag and receive has rule on tag: match 1, match any
  Synch: when send completes, when buffer free, when request accepted, receive wait for send
Send+receive => memory-memory copy, where each each supplies local address, AND does pair-wise synchronization!

## Slide 14: Message Passing Model
Send+receive => memory-memory copy, synchronization on OS even on 1 processor
History of message passing:
  Network topology important because could only send to immediate neighbor
  Typically synchronous, blocking send & receive
  Later DMA with non-blocking sends, DMA for receive into buffer until processor does receive, and then data is transferred to local memory
  Later SW libraries to allow arbitrary communication
Example: IBM SP-2, RS6000 workstations in racks
  Network Interface Card has Intel 960
  8X8 Crossbar switch as communication building block
  40 MBytes/sec per link

## Slide 15: Communication Models
Shared Memory
  Processors communicate with shared address space
  Easy on small-scale machines
  Advantages:
    Model of choice for uniprocessors, small-scale MPs
    Ease of programming
    Lower latency
    Easier to use hardware controlled caching
Message passing
  Processors have private memories, communicate via messages
  Advantages:
    Less hardware, easier to design
    Focuses attention on costly non-local operations
Can support either SW model on either HW base

## Slide 16: Advantages shared-memory communication model
Compatibility with SMP hardware
Ease of programming when communication patterns are complex or vary dynamically during execution
Ability to develop apps using familiar SMP model, attention only on performance critical accesses
Lower communication overhead, better use of BW for small items, due to implicit communication and memory mapping to implement protection in hardware, rather than through I/O system
HW-controlled caching to reduce remote comm. by caching of all data, both shared and private.

## Slide 17: Advantages message-passing communication model
The hardware can be simpler
Communication explicit => simpler to understand; in shared memory it can be hard to know when communicating and when not, and how costly it is
Explicit communication focuses attention on costly aspect of parallel computation, sometimes leading to improved structure in multiprocessor program
Synchronization is naturally associated with sending messages, reducing the possibility for errors introduced by incorrect synchronization
Easier to use sender-initiated communication, which may have some advantages in performance

## Slide 18: References
Laxmi Narayan Bhuyan, http://www.cs.ucr.edu/~bhuyan